TRIPLE RINSING PROCEDURE

FOR CHEMICAL CONTAINERS

- Drain the empty container into the spray tank for 30 seconds

- Fill approximately 20-25% of the container volume with water, replace the lid and rotate the container so all the interior surfaces are rinsed.

- Transfer rinse water into the spray tank, allow draining for at least 30 seconds.

- Repeat the procedure twice more.

- Triple rinsed containers should be placed in allocated secure area until disposal via drumMUSTER

- Containers should not be burned.  Explosions may occur and the smoke and fire products are a risk to health.